## Slide 1: PISCES: A Programmable, Protocol-Independent Software Switch
Muhammad Shahbaz, Sean Choi, Ben Pfaff, Changhoon Kim,
Nick Feamster, Nick McKeown, and Jennifer Rexford
Slide Credit: Muhammad Shahbaz
Notes: Hello, my name is Sean Choi from Stanford University.
Have you ever had ideas for a new protocol, simple additions to current protocol header formats or eliminate some unnecessary fields from the current protocols on a high-performance switch?
Today, I’m will present a tool that adds the flexibility to quickly experiment and deploy a new packet header match and action format on a production level software switch with a very small performance cost to pay for gaining such flexibility. The tool is called PISCES: A Programmable, Protocol Independent Software Switch.
This is a joint work with folks at Princeton, VMware, and Barefoot networks.

## Slide 2: Role of Software Switches
Hypervisor
VM
VM
VM
VM
Hypervisor
VM
VM
VM
VM
VM
VM
VM
VM
Hypervisor
Hypervisor
VM
VM
VM
VM
ToR
ToR
Core
BESS
VPP
Software Switch
OVS
Notes: As more networks transition to virtualized architectures, software switches begin play an increasingly important role both in industry and in research.
To show why software switches are becoming more important, let’s look into the internals of a virtualized network.
When we think of network switches, we tend to think of a physical box in a wiring closet or sitting at the top of a rack of servers.
However, in a virtualized network, a hypervisor, which manages multiple virtual machine, contains a software switch such as Open vSwitch or OVS for routing traffic between the virtual machines and to the outside world.
Because each hypervisor can host as many as 500 virtual machines, we can see how software switches end up being responsible for more networking ports than bare-metal switches.

## Slide 3: Rapid Development & Deployment?
Software Switch
VM
VM
VM
VM
Hypervisor
ToR
I am capable of Rapid Development and Deployment of new protocol header formats!
Not really...
Core
Notes: Previously, in order to deploy the new protocol headers, all hardware and software switches must be upgraded to recognize them correctly.
Now with software switches widely available, we ask the question of how easy it is to make changes to a software switch, to support, and deploy new protocols.
Unfortunately, reprogramming existing software switches can be difficult than one initially imagine it to be.

## Slide 4
Fast Packet IO (or Forwarding)
OVS
Kernel
DPDK
Rapid Development & Deployment?
Notes: One reason why rapid development is difficult is because of their sophisticated internal architecture.
Let’s look at the details of an example software switch to identify why this is a big problem.
Software switches including OVS sit on top of a large body of intricate and complex codebase needed to set up the machinery for fast packet forwarding, which includes Kernel drivers, user-space DPDK, and more.

## Slide 5
Packet Processing Logic
OVS
Kernel
DPDK
Parser
Match-Action Pipeline
Diverse Implementations
Requires domain expertise in:
Network protocol design
Software development
Very Slow Release Cycle
Maintaining changes
Specialized APIs
Rapid Development & Deployment?
Notes: And at the same time, a programmer separately specifies the parser and match action logic for packet processing, using the specialized methods and interfaces exposed by these underlying machinery.
Since programmers are free to choose how they implement these set of requirements, it results in diverse implementations of the same requirements.
In addition, making changes to a software switch require expertise in­ network protocol design and software development.
It can take up to 3-6 months to push a new feature into the mainstream code.
Furthermore, such customization requires not only incorporating the changes into the switch codebase,
but also maintaining those changes, which gets harder as the complexity of these switches increase.

## Slide 6: Needs of Protocol Designers
Kernel
DPDK
Parser
Match-Action Pipeline
OVS
✓
✗
Notes: To identify why this cannot be easily resolved, let’s look at the difference in needs of a protocol designer and a switch developer.
First, a protocol designer is most likely to be only interested in specifying the packet processing logic,
which is the logic to specify which header fields to match and which actions to perform on those matching headers.
However, the same protocol designer most likely does not feel the need to understand how the underlying machinery works.

## Slide 7: What is Protocol-Independence?
Predefined support for protocols
  IPv4, GRE, MPLS,…
Hard to support new protocol header formats
Protocol-Dependent Forwarding Engine
Protocol-Independent Forwarding Engine
VS
Flexible support for protocols
  IPv4_Sean, IPv9,…,GRE_STANFORD
Easy to support new protocol header formats
Notes: To solve this, the idea of protocol-independent forwarding emerged.
Consider a switch or a packet forwarding engine that is capable of forwarding a predetermined set of protocols, such as IPV4, GRE, or MPLS.
It is nearly impossible to quickly add a new packet header format that will make the packet forwarding engine understand what the information contained in the header is for. Thus, we call this type of packet forwarding engine protocol-dependent.
Now consider an different packet forwarding engine that is capable for supporting flexible set of protocols.
We call this type of packet forwarding engine protocol-independent.
So in general, what protocol-independent forwarding is the idea of making the packet forwarding engine programmable, such that it is not tied to a single set of protocols or packet header formats.

## Slide 8: Road to Protocol-Independence
Kernel
DPDK
OVS
Parser
Match-Action Pipeline
Notes: How can we enable protocol-independent forwarding?
The core idea is to separate the packet processing logic and specify it independently of the underlying machinery using a high-level domain-specific language,
where a domain specific language is a computer language specialized to a particular application domain,
and then allow a compiler to generate the resulting logic that can be consumed by the software switch target.
Now we can see that the underlying software switch target is protocol-independent.

## Slide 9: Road to Protocol-Independence
Kernel
DPDK
OVS
Domain-Specific Language
Parser
Match-Action Pipeline
Compile
Parser
Match-Action Pipeline
Notes: How can we enable protocol-independent forwarding?
The core idea is to separate the packet processing logic and specify it independently of the underlying machinery using a high-level domain-specific language,
where a domain specific language is a computer language specialized to a particular application domain,
and then allow a compiler to generate the resulting logic that can be consumed by the software switch target.
Now we can see that the underlying software switch target is protocol-independent.
* Practice this slide more…!

## Slide 10: Road to Protocol-Independence
Kernel
DPDK
OVS
P4[1]
Parser
Match-Action Pipeline
Compile
Parser
Match-Action Pipeline
[1] http://p4.org
Notes: For our work, we chose P4 as our domain-specific language.
P4 is a high-level language specifically designed for programming protocol-independent packet processors.
The language is aimed at easy configuration of custom protocols, parsers and match-action pipeline.
If interested, more information about the language is available at p4.org.
To show how convenient P4 can be, consider this. By taking this approach, we were able to specify the entire packet processing logic of Native OVS in 341 lines of code, where as it can take roughly fourty times more lines of code when writing the same logic using the specialized APIs.
We can see that using P4 clearly has its benefits.

## Slide 11: Benefits to Protocol-Independence
Kernel
DPDK
OVS
P4
Parser
Match-Action Pipeline
Compile
Parser
Match-Action Pipeline
Native OVS
341 lines of code
14,535 lines of code
Notes: To show the benefits of doing this, consider the following. By taking this approach, we were able to specify the entire packet processing logic of Native OVS in 341 lines of code, where as it can take roughly fourty times more lines of code when writing the same logic using the specialized APIs.
We can see that using P4 clearly has its benefits.

## Slide 12: Cost to Protocol-Independence
Kernel
DPDK
OVS
P4
Parser
Match-Action Pipeline
Parser
Match-Action Pipeline
Performance overhead!
Compile
Notes: However, a natural question that arise when presenting this approach is to quantify the performance overhead between a fixed-function switch and a protocol-independent switch.
Since we are automatically compiling a high-level language, in this case P4, down to a lower-level representation, it is safe to reason that there will be some performance difference between these two implementations.
But, the question is by how much? Is it negligible or is it very noticeable?

## Slide 13: Primary Goals
Kernel
DPDK
OVS
P4
Parser
Match-Action Pipeline
Parser
Match-Action Pipeline
Compile
Quantify the Cost on Performance for expressing custom protocols in a Domain Specific Language
Design and evaluate Performance Optimizations to reduce the cost on performance.
Notes: Given this question, our goals are as follow.
Given PISCES, we answer the question of quantifying cost on performance of expressing existing features in a DSL.
In other words, we will quantify the cost of programmability.
Then, we will present methods that we implemented to reduce the performance overhead

## Slide 14: Primary Goals
Quantify the Cost on Performance for expressing custom protocols in a Domain Specific Language
Design and evaluate Performance Optimizations to reduce the cost on performance.
Notes: Our first goal is to quantify the cost on performance

## Slide 15: Quantifying the Cost on Performance
Overview of PISCES architecture
P4 and OVS packet forwarding model
Performance overhead of a naïve mapping from P4 to OVS
Notes: To quantify the cost on performance, I will first give an overview of the PISCES architecture.
Secondly, I will briefly discuss the P4 and OVS packet forwarding model to show the mapping works.
Then, I will present the performance overhead of the naïve mapping between P4 and OVS.

## Slide 16: PISCES Architecture Overview
PISCES
vSwitch
P4
OVS
Notes: PISCES vSwitch works by joining two separate entities. P4 and OVS.
PISCES takes a P4 input as the high-level DSL to express packet processing logic to generate a customized version of OVS.
Given this overall view, the detailed workflow of configuring a PISCES switch.

## Slide 17: PISCES Architecture Overview
Compiler
P4
OVS
parse
match
action
Executable
Notes: First of all, a user provides a P4 program. PISCES’ P4-to-OVS compiler takes the provided P4 code and
generates set of C snippets that can be injected into the appropriate places in the OVS codebase.
The set of codes that are generated corresponds to functions that perform [CLICK]
parse, match and actions on the packet.
After injecting the code, the workflow is to execute the traditional compilation procedure of OVS [CLICK]
And generate set of OVS executables that look exactly the same as the vanilla OVS executables.
This is the entire workflow of generating a protocol-independent version of OVS given a P4 program.
We can simply run this workflow again with a new P4 program, and this workflow takes around 20~30 seconds from start to finish.

## Slide 18: P4 Forwarding Model
Packet
Parser
Match-Action
Tables
Packet
Deparser
Ingress
Egress
Header
Fields
Ingress Packet
Egress Packet
Checksum
Update
Checksum
Verify
(Post-Pipeline Editing)
Notes: Now I will talk about the two different forwarding models to give you an idea of how the mapping from P4 to OVS is done.
First I will talk about the P4 forwarding model.
In P4 packet forwarding model, [click] a packet parser [click] identifies the headers and [click] extracts them as packet header fields (i.e., essentially a copy of the content of the packets). [click] The checksum verify block then [click] verifies the checksum based on the header fields specified in the P4 program. [click] The match-action tables [click] operate on these header fields. [click] A checksum update block [click] updates the checksum. [click] Finally, a packet deparser [click] writes the changes from these header fields back on to the packet. [click] We name this mode of operating on header fields as “post-pipeline editing.”

## Slide 19
Packet
Parser
Ingress
Match-Action
Cache
Egress Packet
Ingress Packet
Egress
Miss
Match-Action
Tables
Flow Rule
OVS Forwarding Model
Notes: Whereas, in OVS packet forwarding model, [click] a packet parser only [click] identifies the headers. The [click] packet is then looked up in a match-action cache. If there is a [click] miss, the is sent to the match-action tables (that form the actual switch pipeline). [click] A new flow rule is calculated and installed in the match-action cache. [click] And the original packet, as processed by the match-action pipeline is sent to the egress.

## Slide 20
Packet
Parser
Ingress
Match-Action
Cache
Egress
Match-Action
Tables
Egress
(Inline Editing)
Egress Packet
OVS Forwarding Model
Notes: In OVS, tables directly operate on the headers inside the packet (i.e., not copy is maintained). We name this mode of operating on packet header fields as “inline editing.”

## Slide 21
Packet
Parser
Ingress
Match-Action
Cache
Match-Action
Tables
Packet
Deparser
Egress
Supports both editing modes:
  Inline Editing
  Post-pipeline Editing
Checksum
Verify
Checksum Update
PISCES Forwarding Model (Modified OVS)
Notes: So, in order to map P4 to OVS, we modified the OVS to provide support for both these editing modes. We call this modified OVS model, a PISCES forwarding model.

## Slide 22
Packet
Parser
Match-Action
Tables
Packet
Deparser
Ingress
Egress
Checksum
Update
Checksum
Verify
Packet
Parser
Ingress
Match-Action
Cache
Match-Action
Tables
Packet
Deparser
Egress
Checksum
Verify
Checksum Update
P4
modified
OVS
PISCES: Compiling P4 to OVS
Notes: So, now the problem is how to efficiently compile the P4 forwarding model [click] to this modified OVS forwarding model.

## Slide 23: What is the Cost on Performance?
Chart: Packet Size (Bytes)
| 64.0 | 128.0 | 192.0 | 256.0
PISCES (naïve) | 8288.9826 | 13620.3633 | 18999.7122 | 25710.3289
OVS | 13431.6165 | 23346.1018 | 33174.8183 | 43001.7233
A naïve compilation of L2L3-ACL benchmark application shows …
Performance overhead of
~ 40%
Notes: A naïve compilation of L2L3-ACL benchmark application, which is essentially the test that
measures throughput through a router with access-control list, shows [CLICK]
that PISCES has a throughput of roughly 40% less than the native OVS.

## Slide 24: Primary Goals
Quantify the Cost on Performance for expressing custom protocols in a Domain Specific Language
Design and evaluate Performance Optimizations to reduce the cost on performance.
Notes: Given the overhead shown in the naïve compilation,
Our second goal is to present our methods of making performance optimizations.

## Slide 25
Packet
Parser
Ingress
Match-Action
Cache
Match-Action
Tables
Packet
Deparser
Egress
Checksum
Verify
Checksum Update
CPU Cycles per Packet
Cache Misses
Causes for the Cost on Performance
Notes: We observe that there are two main aspects that significantly affect the performance of PISCES.
[click]
The first one is the number of CPU cycles consumed in processing a single packet.
[click]
And the second one is the number of cache misses.
For this talk, I will limit to talking only about the CPU cycles per packet.

## Slide 26
Switch | Optimization | Parser (Cycles) | Match-Action Cache (Cycles) |  | Throughput (Mbps)
 |  |  | Match | Actions | 
PISCES | Without optimizations | 76.5 | 209.5 | 379.5 | 7590.7
OVS | Native | 43.6 | 197.5 | 132.5 | 13497.5
A naïve compilation of L2L3-ACL benchmark application
Cause: CPU Cycles per Packet
Notes: In terms of the number of CPU cycles, for L2L3-ACL …

## Slide 27
2x
Switch | Optimization | Parser (Cycles) | Match-Action Cache (Cycles) |  | Throughput (Mbps)
 |  |  | Match | Actions | 
PISCES | Without optimizations | 76.5 | 209.5 | 379.5 | 7590.7
OVS | Native | 43.6 | 197.5 | 132.5 | 13497.5
A naïve compilation of L2L3-ACL benchmark application
Cause: CPU Cycles per Packet
Notes: PISCES consumes roughly two times more cyles in parsing and actions, when compiled without optimizations, and the throughput is two times less than the native OVS.

## Slide 28
Extra copy of headers
Fully-specified Checksum
Parsing unused header fields
and more …
Factors affecting CPU Cycles per Packet
Notes: We studied different factors that affected the CPU cycles per-packet [click] like …
I will now talk about each of them in detail and how we optimized them in PISCES.

## Slide 29
For example, Post-pipeline editing consumes 2x more cycles than inline editing when parsing VXLAN protocol.
Editing Mode | Pros | Cons
Post-Pipeline |  | Extra copy of headers
Inline | No extra copy of headers | 
Factor: Extra Copy of Headers
Notes: P4, by default, assumes a post-pipeline editing, thus, it requires keeping an extra copy of headers as shown earlier.
[click]
The post-pipeline editing mode requires maintaining an extra copy of headers. Whereas, inline editing mode doesn’t require any extra copy.
We found that maintaining these extra copies has a significant overhead.
[click]
For example, while using a tunneling protocol (like VXLAN), the post-pipeline editing mode consumed two times more cycles than inline editing mode.

## Slide 30
Editing Mode | Pros | Cons
Post-Pipeline | Packet is adjusted once | Extra copy of headers
Inline | No extra copy of headers | Multiple adjustments to packet
Chart: Number of adjustments
| Deparse | x1 | x2 | x4 | x8 | x16
Post-Pipeline Editing | 99.72 | 134.76 | 136.3 | 138.44 | 143.23 | 144.59
Inline Editing | 0 | 74.93 | 109.1 | 181.41 | 326.64 | 711.54
Inline editing
Post-pipeline editing
Factor: Extra Copy of Headers
Notes: But, on the other hand, in case of post-pipeline editing, packet is adjusted only once, i.e., changes are applied only once at the end of the match-action pipeline. Whereas, in case of inline editing, packet is adjusted (and changes are applied) on every action.
[click]
Adjusting packets has a very high toll on performance, as can be seen in the graph here.
[click]
Based on our micro-benchmarks, we observe that if the number of adjustments are less than six, we should use inline editing otherwise [click] we should use post-pipeline editing mode.

## Slide 31
Switch | Optimization | Parser (Cycles) | Match-Action Cache (Cycles) |  | Throughput (Mbps)
 |  |  | Match | Actions | 
PISCES | Without optimizations Inline Editing | 76.5 -42.6 | 209.5 – | 379.5 +7.5 | 7590.7 +281.0
Cycles per packet and throughput of L2L3-ACL application
Editing Mode Optimization
Notes: So with the inline editing optimization, we were able to reduce the CPU cycles during the parsing to increase the throughput.

## Slide 32
Packet
Parser
Ingress
Match-Action
Pipeline
Egress
Checksum
Verify
Checksum Update
Checksum Verify (
version, ihl, diffserv, totalLen,
identification, flags, fragOffset,
ttl, protocol, hdrChecksum,
srcAddr, dstAddr)
Checksum Update (
version, ihl, diffserv, totalLen,
identification, flags, fragOffset,
ttl, protocol, hdrChecksum,
srcAddr, dstAddr)
Factor: Fully Specified Checksum
Notes: P4 requires a programmer to fully specify which fields to use when computing a checksum.
For example, in case of IP the programmer has to specify all 12 fields of the IP header.
A naïve compilation would end up generating code that would compute checksum over all the header fields for each incoming packet
even if only a subset of these fields have been modified in the match-action pipeline. This is inefficient and can consume precious CPU cycles

## Slide 33
Provided annotations to let the programmer inform the compiler whether the switch:
  Is a part of an “end-host stack”
  Is running as a “transit switch”
Optimization: Incremental Checksum
Notes: In order to optimize this, we added the notion of incremental checksum based on what the switch operates as.
First we allowed the programmer to select the switch modes at compile time to configure the switch to be a part of an end-host stack or to run as a transit switch.
For each of these different modes, we provided the following optimizations

## Slide 34
If part of an “end-host stack”
Packet
Parser
Ingress
Match-Action
Pipeline
Egress
Checksum
Verify
Checksum Update
Checksum Verify (
version, ihl, diffserv, totalLen,
identification, flags, fragOffset,
ttl, protocol, hdrChecksum,
srcAddr, dstAddr)
Checksum Update (
version, ihl, diffserv, totalLen,
identification, flags, fragOffset,
ttl, protocol, hdrChecksum,
srcAddr, dstAddr)
✗
Optimization: Incremental Checksum
Notes: When running as an end-host stack, the switch only needs to verify the checksum, so we configured the switch to eliminate checksum update.

## Slide 35
Packet
Parser
Ingress
Decrement(ttl)
Egress
Checksum
Verify
Checksum Update
Checksum Verify (
version, ihl, diffserv, totalLen,
identification, flags, fragOffset,
ttl, protocol, hdrChecksum,
srcAddr, dstAddr)
Incremental Checksum Update (ttl)
✗
If running as a “transit switch”
Optimization: Incremental Checksum
Notes: When running as a transit switch, the switch only needs to update the checksum, so we configured the switch to eliminate checksum verify.
In addition, if the switch is doing a very simple operation on one of the fields, for example decrement ttl, we implemented the incremental checksum method to update the checksum based on the single field.

## Slide 36
Switch | Optimization | Parser (Cycles) | Match-Action Cache (Cycles) |  | Throughput (Mbps)
 |  |  | Match | Actions | 
PISCES | Without optimizations Inline Editing Inc. Checksum (running as a Transit Switch) | 76.5 -42.6 – | 209.5 – – | 379.5 +7.5 -231.3 | 7590.7 +281.0 +4685.3
Cycles per packet and throughput of L2L3-ACL application
Optimization: Incremental Checksum
Notes: By doing this, our experiment showed a huge decrease in the CPU cycles needed in the match-action pipeline.

## Slide 37: Factor: Parsing Unused Header Fields
Packet
Deparser
Egress
Packet
Parser
Ingress
Match-Action
Pipeline
L2
L2
L4
L3
Notes: Our third optimization is parser optimization.
Parser specialization is the process of optimizing the parser, so that it only extracts fields that are actually used by the match-action pipeline.
[CLICK]
For example, if we are only using L2 headers in the match-action pipeline then, in that case, [CLICK]
the parser shouldn’t have to extract L3 and L4 headers.

## Slide 38
Switch | Optimization | Parser (Cycles) | Match-Action Cache (Cycles) |  | Throughput (Mbps)
 |  |  | Match | Actions | 
PISCES | Without optimizations Inline Editing Inc. Checksum (Transit Mode) Parser Specialization | 76.5 -42.6 – -4.6 | 209.5 – – – | 379.5 +7.5 -231.3 – | 7590.7 +281.0 +4685.3 +282.3
Cycles per packet and throughput of L2L3-ACL application
Optimization: Parser Specialization
Notes: By adding parser specialization, we again reduced some number of CPU cycles when parsing each packet.

## Slide 39
Switch | Optimization | Parser (Cycles) | Match-Action Cache (Cycles) |  | Throughput (Mbps)
 |  |  | Match | Actions | 
PISCES | Without optimizations Inline Editing Inc. Checksum (Transit Mode) Parser Specialization Action Specialization Action Coalescing | 76.5 -42.6 – -4.6 – – | 209.5 – – – – – | 379.5 +7.5 -231.3 – -10.3 -14.6 | 7590.7 +281.0 +4685.3 +282.3 +191.2 +293.0
Cycles per packet and throughput of L2L3-ACL application
Optimization: Action Improvements
Notes: We added two more improvements regarding actions.
If interested, more details are available on our paper.

## Slide 40
Switch | Optimization | Parser (Cycles) | Match-Action Cache (Cycles) |  | Throughput (Mbps)
 |  |  | Match | Actions | 
PISCES | Without optimizations Inline Editing Inc. Checksum (Transit Mode) Parser Specialization Action Specialization Action Coalescing | 76.5 -42.6 – -4.6 – – | 209.5 – – – – – | 379.5 +7.5 -231.3 – -10.3 -14.6 | 7590.7 +281.0 +4685.3 +282.3 +191.2 +293.0
 | All optimizations | 29.7 | 209.0 | 147.6 | 13323.7
OVS | Native | 43.6 | 197.5 | 132.5 | 13497.5
Final Result
Notes: So, after all the optimizations, here are the numbers. As you can see the Throughput numbers are very close.
Also, we can see that there are still room for improvements on the Match and action CPU cycles compared to Native OVS.

## Slide 41: Optimized Mapping from P4 to OVS
Chart: Packet Size (Bytes)
| 64.0 | 128.0 | 192.0 | 256.0
PISCES (unoptimized) | 8288.9826 | 13620.3633 | 18999.7122 | 25710.3289
PISCES (Optimized) | 13323.6646 | 22457.3254 | 31323.1518 | 41981.917
OVS | 13431.6165 | 23346.1018 | 33174.8183 | 43001.7233
Performance overhead of
< 2%
An optimized compilation of L2L3-ACL benchmark application
Notes: After applying all these optimizations, we see that the performance overhead is now less than 2% between the optimized version of PISCES and the native OVS.
So, this shows that with appropriate compiler optimizations the cost of programmability on performance is negligible.
This gap is predicted to get smaller as we identify and add more optimizations in the future.

## Slide 42: Summary
PISCES
vSwitch
OVS
P4
PISCES programs are 40 times more concise than the same logic in the native language
With hardly any performance cost!
Notes: In summary, [CLICK]
We presented PISCES, the first protocol-independent software switch
that allows specifying a software switch’s custom packet processing in a high-level DSL, called P4. [CLICK]
PISCES programs are about 40 times more concise than the equivalent programs in native language of the software switch
[CLICK] with only 2% performance cost, which is projected to decrease with more optimizations
Is is too early to see the effects PISCES on protocol development,
but the resulting code simplicity should make it easier to implement, maintain, and deploy new features.
We plan to interact and work closely with protocol designers who use PISCES
to study and accumulate their experience and measure reduction in deployment, implementation and maintenance time in order to validate the utility of PISCES.

## Slide 43: Questions?
              Learn more and try PISCES here:
              http://pisces.cs.princeton.edu
Notes: With this I conclude my presentation. Thank you, and I’m happy to take any questions.